## Slide 1: Lab 1 : Introduction to Arduino
Asst. Prof. Dr.Sumek Wisayataksin
Faculty of Engineering
King Mongkut’s Institute of Technology Ladkrabang

## Slide 2: What is an Arduino ?
Open Source electronic prototyping platform based on flexible easy to use hardware and software.

## Slide 3: History

## Slide 4: Type of Arduino
Arduino Uno Rev3
The Uno is a huge option for your initial Arduino. It consists of
14-digital I/O pins, where 6-pins can be used as PWM(pulse width modulation outputs)
6-analog inputs, a reset button
a power jack, a USB connection.
PC connection via USB cable

## Slide 5: Arduino Uno Rev3 Specification

## Slide 6: Microcontroller Before Arduino Board

## Slide 7: Microcontroller Before Arduino Board
Assembly Programming

## Slide 8: Microcontroller Before Arduino Board

## Slide 9: Other Arduino Boards and Microcontrollers
Arduino Nano
Arduino Mega
Arduino Uno WIFI
NodeMCU ESP32
- Xtensa dual-core (or single-core) 32-bit LX6 microprocessor, operating at 160 or 240 MHz
- Wi-Fi: 802.11 b/g/n
- Bluetooth: v4.2 BR/EDR and BLE
520 KiB SRAM

## Slide 10: Arduino Board Comparison

## Slide 11: Arduino Uno Structure

## Slide 12: Arduino IDE -> www.arduino.cc

## Slide 13: Arduino IDE
Compile Code
Upload Code
(Program Flash Memory

## Slide 14: Arduino IDE
Select Board

## Slide 15: Arduino IDE
Select Serial Port Connection

## Slide 16: Arduino Programming
Bare minimum code
void setup() { // put your setup code here, to run once:
}
void loop() { // put your main code here, to run repeatedly:
}

## Slide 17: Bare minimum code
setup : It is called only when the Arduino is powered on or reset. It is used to initialize variables and pin modes
loop : The loop functions runs continuously till the device is powered off. The main logic of the code goes here. Similar to while (1) for micro-controller programming.

## Slide 18: PinMode
A pin on Arduino can be set as input or output by using pinMode function.
pinMode(13, OUTPUT); // sets pin 13 as output pin
pinMode(13, INPUT); // sets pin 13 as input pin

## Slide 19: Writing Digital Values
digitalWrite(13, LOW); // Makes the output voltage on pin 13 , 0V
digitalWrite(13, HIGH); // Makes the output voltage on pin 13 , 5V

## Slide 20: LED (Light-Emitting Diode)
a semiconductor light source that emits light when current flows through it.
The color of the light (corresponding to the energy of the photons) is determined by the energy required for electrons to cross the band gap of the semiconductor.

## Slide 21: LAB 1.1 : LED Control
Breadboard

## Slide 22: Breadboard or Protoboard

## Slide 23: LAB 1.1 : LED Control
void setup()
{
pinMode(13, OUTPUT);
}
void loop()
{
digitalWrite(13, HIGH);
delay(1000);
digitalWrite(13, LOW);
delay(1000);
}
220 Ohm

## Slide 24: How to compile and upload code

## Slide 25: How to submit your work
1. Submit your code.

## Slide 26: How to submit your work
2. Submit your hardware pictures.

## Slide 27: How to submit your work
3. Submit video showing how it works (with yourself in the video).

## Slide 28: Reading Digital Values
pinMode(2, INPUT); // sets pin 2 as input pin
buttonState = digitalRead(2); // reads the value of pin 2

## Slide 29: Push Button
Not Push
Push
Open Circuit
Short Circuit

## Slide 30: Push Button
GND (Logic 0)
5V (Logic 1)
Arduino Input
GND
(Logic 0)
5V (Logic 1)
Not Push
Arduino Input
Logic ???
GND
(Logic 0)
5V (Logic 1)
Push
Arduino Input
Logic ???

## Slide 31: LAB 1.2 : Reading Digital Values
10kOhm
220Ohm
char status;
void setup()
{
pinMode(13,OUTPUT);
pinMode(2, INPUT);
}
void loop()
{
status = digitalRead(2);
// Add your code here
}

## Slide 32: Arduino C Variables
char : 8-bit number value from -128 to 127.
unsigned char : 8-bit number from 0 to 255.
int : 16-bit number from -32768 to 32767.
unsigned int : 16-bit number from 0 to 65536.
float : real number with floating point.

## Slide 33: Basic C Structure
While loop
While (digitalRead(2)==1)
{
// Do until digitalRead(2)!=0
}

## Slide 34: Basic C Structure
For loop
char i;
for (i=0;i<10;i++);
{
// Do from i==0 until i==9
// Totally 10 times
}

## Slide 35: Basic C Structure
If statement
if (digitalRead(2)==1)
{
// Do when digitalRead(2) == 1;
}
else
{
// Do when digitalRead(2) == 0;
}

## Slide 36: Basic C Structure
switch statement
char case;
switch (case)
{
case 0 : { // Do something; break;}
case 1 : { // Do something; break;}
case 2 : { // Do something; break;}
case 3 : { // Do something; break;}
default : { // Do something; break;}
}

## Slide 37: LAB 1.3 : Arduino Port Test
Condition
Connect Arduino with 3 LEDs : Red, Yellow and Green.
Connect 1 push button.
When Arduino starts no LED on.
When button is pushed and released -> Red on, Yellow off , Green off
When button is pushed and released again -> Red Off, Yellow on , Green off
When button is pushed and released again -> Red Off, Yellow off , Green on
When button is pushed and released again -> Back to 4.

## Slide 38: LAB 1.3 : Arduino Port Test

## Slide 39: LAB 1.3 : Arduino Port Test