## Slide 1: Arduino Lab 4 : Temperature Sensor , LCD and Soldering
Asst. Prof. Dr.Sumek Wisayataksin
Faculty of Engineering
King Mongkut’s Institute of Technology Ladkrabang

## Slide 2: Sensor
A Sensor converts the physical parameter (for example : temperature, blood pressure, humidity, speed, etc.) into a signal which can be measured electrically.
Light Dependent Resistor
Temperature Sensor
Infrared Sensor

## Slide 3: Light Sensor
Light-Dependent Resistor (LDR) : The resistance will decrease according to the light intensity. It can be 15Mohm when no light and become 15 Kohm when light detected.
Light Dependent Resistor

## Slide 4: Temperature Sensor
LM35 will increase 10mV every 1c.
For example : 0v at 0c
250mv at 25c

## Slide 5: Infrared Sensor
Notes: We can check the distance by using VST operations. This will allow the card to turn automatically with some coding.

## Slide 6: How to connect sensor to microprocessor
Heat
Heat Sensor
Electric Voltage/Current
(Analog)
Binary Representation
(Digital)
Digital Signal Processing
Binary Response
(Digital)
Electric Voltage/Current
(Analog)
Analog World
Digital World

## Slide 7: DHT11 Temperature Sensor
Digital-output relative humidity & temperature sensor.

## Slide 8: Serial Communication
serial communication is the process of sending data one bit at a time, sequentially, over a communication channel or computer bus.
0b11010010 = 0xD2 = 210
BIN
HEX
DEC

## Slide 9: Parallel Communication
parallel communication is a method of conveying multiple binary digits (bits) simultaneously.
0b10110100 = 0xB4 = 180

## Slide 10: LCD Display
It is a simplest display with 16 Character x 2 Line.
Easy to Control using a parallel port.

## Slide 11: LCD Display
VSS : GND
VCC: 5V
VEE : Contrast Adjust
RS : Register Select
RS = 0 : Command
RS = 1 : Data
RW : Read/ Write
RW = 0 : Write
E : Enable
D7-D0 : Parallel Data
LED+/- : Backlight

## Slide 12: Lab 4.1 : Thermometer
Connect DHT22 and LCD to Arduino as shown below.
7
5v
GND
GND 5V 12 GND 11 5 4 3 2 5V GND
5V
GND

## Slide 13: Lab 4.1 : Thermometer
Install DHT22 Library go to canvas and copy DHT_lib.zip
Download and Unzip

## Slide 14: Lab 4.1 : Thermometer
Install the Library
Add .ZIP Library
Select downloaded file

## Slide 15: Lab 4.1 : Thermometer
Write this code
You should see Temperature and Humidity showed on LCD !!!

## Slide 16: Lab 4.1 : Thermometer

## Slide 17: Soldering
process in which two or more items are joined together by melting and putting a filler metal (solder) into the joint.

## Slide 18: Soldering
Soldering Iron

## Slide 19: Soldering
Soldering Lead
Soldering Flex
Desoldering Pump

## Slide 20: How to Do Soldering

## Slide 21: How to Do Desoldering

## Slide 22: Good Soldering Point

## Slide 23: Lab 4.2 : Ohmmeter
GND 5V 12 GND 11 5 4 3 2 5V GND
5V
GND
Resistance
x.xx KOhm
GND
5V
10k
R??
A0

## Slide 24: Lab 4.2 : Ohmmeter
V = (5*D)/1024
Convert V to R from ohm law
Display it in LCD
Convert integer to float  float d_float = (float)D;
Convert float to string  dtostrf(val,10,2,str);
Create the sentence  sprintf();