## Slide 1: Arduino Lab 6 : Motor
Asst. Prof. Dr.Sumek Wisayataksin
Faculty of Engineering
King Mongkut’s Institute of Technology Ladkrabang

## Slide 2: Motor
Servo Motor. Stepper Motor. DC Motor.

## Slide 3: Servo Motor
A servo-motor is an actuator with a built-in feedback mechanism that responds to a control signal by moving to and holding a position, or by moving at a continuous speed.

## Slide 4: Servo Motor
Two types of servos
continuous rotation
pulse tells servo
which way to spin & how fast to spin
pulse tells servo
which position to hold
standard
can only rotate 180 degrees
can rotate all the way around in either direction

## Slide 5: Servo Motor
How to control the angle
Pulse frequency is fixed
Typical: 20 ms
Pulse width determines position
Typical: 1ms to 2 ms

## Slide 6: Servo Motor
Application

## Slide 7: Servo Motor
Application

## Slide 8: Servo Motor
Connection

## Slide 9: Servo Motor
Arduino Servo library
Three components of the Servo Library
  Create the servo object
    Servo my_servo_object;
  Attach the object
    my_servo_object.attach(servo_pin);
  Send control signal
    my_servo_object.write(pos);
Name of the object is like a variable name.
attach and write are pre-defined methods that act on the servo object.

## Slide 10: Servo Motor
Servo Motor Code Sample
White Pin

## Slide 11: Lab 6.1 : Servo Motor
White Pin
Control Servo motor using push button.
Angle starts at 0 degree. Every time button is pushed, angle increases 45 degree.
When angle become 180 degree, decrease 45 degree until 0 degree.
Show the angle on Serial port.
0 -> 45 -> 90 -> 135 -> 180 -> 135 -> 90 -> 45 -> 0 > ….

## Slide 12: Stepper Motor
DC motors with precise control of how far they spin.
They have a fixed number of “steps” the take to turn one full revolution.
You can control them one step at a time.
Makes for very precise and repeatable positioning.

## Slide 13: Stepper Motor
Very precise.
Much stronger than servos, but they use more current.
a little tricky to drive.

## Slide 14: Stepper Motor
How do they work ?
 | in1 | in2 | in3 | In4
Phase 1 | 1 | 0 | 0 | 0
Phase 2 | 0 | 1 | 0 | 0
Phase 3 | 0 | 0 | 1 | 0
Phase 4 | 0 | 0 | 0 | 1
in1
in2
in3
in4
FULL STEP

## Slide 15: Stepper Motor
How do they work ?
 | in1 | in2 | in3 | In4
Phase 1 | 1 | 0 | 0 | 0
Phase 2 | 1 | 1 | 0 | 0
Phase 3 | 0 | 1 | 0 | 0
Phase 4 | 0 | 1 | 1 | 0
Phase 5 | 0 | 0 | 1 | 0
Phase 6 | 0 | 0 | 1 | 1
Phase 7 | 0 | 0 | 0 | 1
Phase 8 | 1 | 0 | 0 | 1
HALF STEP
in1
in2
in3
in4

## Slide 16: Stepper Motor
Applications

## Slide 17: Stepper Motor
Applications

## Slide 18: Lab 6.2 : Stepper Motor
Connection

## Slide 19: Lab 6.2 : Stepper Motor
Code
Find a number to make the stepper motor turns
360, 180, 90 and 45 degree

## Slide 20: DC Motor
It is a machine which convert electrical energy into mechanical energy.
DC motor means a motor that runs on direct current (DC) electricity.

## Slide 21: DC Motor
How do they work ?

## Slide 22: DC Motor
Application

## Slide 23: DC Motor
Applications

## Slide 24: DC Motor
Connection
3
2
Use Adapter for high power

## Slide 25: DC Motor
Sample Code

## Slide 26: Lab 6.3 DC Motor
1
2
3

## Slide 27: Lab 6.3 DC Motor
Control DC motor speed using “analogWrite”.
Speed control from potentiometer (leftmost -> stop, rightmost -> fastest)
Push button is used to change the direction (clockwise -> counterclockwise -> clockwise).
Showing spin direction and speed in percent in a serial monitor.
clockwise 30%
Example