## Slide 1: Lab 3 : Analog Signal and Serial Interface
Asst. Prof. Dr.Sumek Wisayataksin
Faculty of Engineering
King Mongkut’s Institute of Technology Ladkrabang

## Slide 2: Lab 2.3 : 7-Segment Countdown

## Slide 3: Lab 2.3 : 7-Segment Countdown

## Slide 4: Digital Signal
Digital signal has only 2 level of voltages. We represent them as logic 1 and logic 0
0V
5V
logic1
logic0

## Slide 5: Analog Signal
Analog signal is a continuous signal that has unlimited level of voltage.
5V
0V
2.5957 v
4.35824v

## Slide 6: Use Arduino to Read/Write Digital Signal
Arduino has 14 Digital Ports.
WRITE : digitalWrite(PORT, 0/1);
READ : digitalRead(PORT);
0V
5V
logic1
logic0

## Slide 7: Use Arduino to Read Analog Signal
Arduino has 5 Digital Ports.
READ : analogRead(PORT);
A0-A5
5V
0V

## Slide 8: Potentiometer
Potentiometer is an adjustable resistor. You can choose the resistance that you want by moving like a volume.

## Slide 9: Potentiometer
Potentiometer looks like 2 resistors connected in series.
5V
0V
RA
RB
1
2
3
2
3
1
1
2
3

## Slide 10: Lab 3.1 : analogRead
GND
5V
A0
1
2
3
Notes: You can also get at a maximum 10 bit number from using the analogRead() function. If you want a decimal number, use float instead of int.

## Slide 11: Serial Communication
Universal Asynchronous Receiver-Transmitter (UART)

## Slide 12: Serial Communication
Universal Asynchronous Receiver-Transmitter (UART)
Standard BAUD Rate :
110,300,600,1200,2400,4800,9600,
14490,19200,38400,57600,115200,
12800,256000

## Slide 13: Serial Communication
UART to USB Converter

## Slide 14: Serial Communication
UART to Bluetooth Module
Bluetooth
Bluetooth

## Slide 15: Arduino Serial Monitor
Used for communication between the Arduino board and a computer or other devices. All Arduino boards have at least one serial port (also known as a UART)
9600 means 9600 bit per second
The speed is sometimes called BAUDRATE

## Slide 16: Arduino Serial Monitor

## Slide 17: Arduino Serial Monitor
sprintf function : use for create the text.
char text[30]; // 30 character string
int value = 50;
sprintf(text, “This value is %d”, value);
Serial.println(text); // This value is 50
Show value in decimal

## Slide 18: Arduino Serial Monitor
sprintf function : use for create the text.
char text[30]; // 30 character string
char name[20] = “Uncle Prayut”;
char value = 3000;
sprintf(text, “I love %s %d”, name,value);
Serial.println(text); // I love Uncle Prayut 3000
Show string
Show decimal

## Slide 19: Arduino Serial Monitor
sprintf function : use for create the text.
char text[30]; // 30 character string
float pi = 3.1415;
sprintf(text, “Pi number is %f”, pi);
Serial.println(text); // Pi number is 3.1415
Show string
Show decimal

## Slide 20: Arduino Serial Monitor
sprintf format
%d : Decimal
%x : Hexadecimal
%f : floating point
%s : String
%c : 1 character
unsigned char val = 78;
char text[30];
sprintf(text, “%d”, val); // 78
sprintf(text, “%x”, val); // 4E
sprintf(text, “%c”, val); // N
val = ‘a’;
sprintf(text, “%d”, val); // 97
sprintf(text, “%x”, val); // 61
sprintf(text, “%c”, val); // a

## Slide 21: Ascii Table

## Slide 22: Arduino Serial Monitor
Tool -> Serial Monitor

## Slide 23: Lab 3.1 : analogRead
No | Analog Voltage | Digital
1 | 0v | 0
2 | 0.5v | 106
3 | 1v | 195
4 | 1.5v | 302
5 | 2v | 403
6 | 2.5v | 505
7 | 3v | 612
8 | 3.5v | 713
9 | 4v | 820
10 | 4.5V | 924
11 | 5v | 1023
Notes: Float a = D/1024 * 5.0

## Slide 24: Lab 3.1 : analogRead
Plot graph to show the relation between Analog voltage and digital number
0 0.5 1 1.5 2 2.5 3 3.5 4 4.5 5
Analog Voltage
Digital Number
100
200
300
400
500
600
700
800
900
1000
1100

## Slide 25: Lab 3.1 : analogWrite
GND
5V
A0
Voltmeter
GND
+
-
(11,OUTPUT);
(11,________);
Notes: analogWrite(outputPIN,a/4) where a is equal to the serial read value(). This allows the LED to dim according to the value given.

## Slide 26: Lab 3.1 : analogWrite
No | analogWrite(11,v) | Port 11 Voltage
1 | 0 | 
2 | 63 | 
3 | 127 | 
4 | 195 | 
5 | 255 | 
6 | 256 | 
7 | 319 | 
8 | 383 | 
9 | 447 | 
10 | 511 | 
11 | 512 | 

## Slide 27: Lab 3.1 : analogWrite
0 63 127 195 255 319 383 447 511
analogWrite(11,v)
Analog Output
0.5
1.0
1.5
2.0
2.5
3.0
3.5
4.0
4.5
5.0
5.5

## Slide 28: Analog Write
GND
5V
A0
GND
220
1. Write a program to dim the LED brightness from the potentiometer. When turn the potentiometer to the leftmost, LED off, when turn potentiometer to the right, LED get bright and becomes brightest when potentiometer on the rightmost position.
2. Showing this String on serial monitor
LED brightness level is xxx%
int val = AnalogREAD(A0);
unsigned char dim = map(val,0,1023,0,255);
AnalogWRITE(11,dim);

## Slide 29: Light Dependent Resistor
An LDR or light dependent resistor is also known as photo resistor, photocell, photoconductor. It is a one type of resistor whose resistance varies depending on the amount of light falling on its surface.

## Slide 30: Serial Read
We can use serial to read data from PC.
char val = Serial.read(); // This will read 1 byte data
String text = Serial.readString(); // This will read 1 line text;
text.replace(“\n”,””) // To remove newline
void serialEvent() {
// Rx callback function. It will jump to this function, if
// Arduino receives data from PC.
}

## Slide 31: Light Dependent Resistor
Automatic Street Light Control
220
Notes: Around 600 and 900 (750 threshold)

## Slide 32: Lab 3.2 : Light Dependent Resistor
Use LDR and Serial Command to control LED
There are 3 Modes
LED on
LED off
LED controlled by LDR
- When it is dark, LED on.
- When it is Bright, LED off.
5V
GND
10k
GND
220

## Slide 33: Lab 3.2 : Light Dependent Resistor
--- Control LED mode from PC ---
>> Select LED Mode (on,off,ldr) : on
LED is ON
>> Select LED Mode (on,off,ldr) : off
LED is OFF
>> Select LED Mode (on,off,ldr) : ldr
LED is controlled by LDR
>> Select LED Mode (on,off,ldr) : aaacccffgg
Wrong Commend
>> Select LED Mode (on,off,ldr) :
Notes: Control the LED on the serial monitor prompt